## Slide 1: Level up Asset Management at Infrabel
Image recognition, AI & IOT projects
Mathias Vanden Auweele
Project lead, Infrabel, I-AM.2

## Slide 2: Overview
Infrabel
Smart projects overview
How to locate an infrastructure problem using GPS stamped data?

## Slide 3: Infrabel
We manage, maintain and modernise
the Belgian railway infrastructure
We coordinate rail traffic
on the Belgian network
~11k employees FTE
~800k passengers daily
~6500 km main track
~5800 km electrified
~4k switches
And we do it ourselves..

## Slide 4: Switch
-> 400 switches equipped
-> Predictive maintenance
-> 75% of mechanical failures predicted
-> Link with train routes traffic control
IoT on point machines. Real time monitoring of condition of turnout / railway switch
Real-time data to diagnostics system and processing by Operation Center
Worm gear
Bad alignment
Wear on
Sliders

## Slide 5
-> AI
-> Deep learning / machine learning
-> Unsupervised-learning -> Dimensionality reduction using neural networks
IoT on point machines. Real time monitoring of condition of turnout / railway switch
Normal data
Over Current
Not locking
Switch

## Slide 6: Pantograph shock detection
For 2018:
-> 11 commercial vehicles
-> More than 1M km inspected
-> 261k shock alerts received
-> Grouped to 22k locations
-> 472 workorders created
Fully automated from alert to workorder
IoT on commercial trains. Real time detection of catenary problems.

## Slide 7: CatVision
Home made vision systems for catenary applications

## Slide 8: Switch
-> target : 4000 switches
-> 1 automated control / year
-> data cel defect verification
-> laser measurements
-> HD video from different angles
Measuring train : Automated measuring and visual inspection of condition of turnout / railway switch
  5 cameras associated with 3 lasers per rail

## Slide 9
Lidar vegetation detection
Classify vegetation according to distance and height
Raw lidar measurement on train
4 sweeps / meter
1001 measurements / sweep
About 2 data collections per year
Detect vegetation in point cloud

## Slide 10: Train monitoring system
Currently for one type pantograph:
3mm accurate carbon thickness
10% false/positive & false/negative
Deformation check

## Slide 11: SpadWatch
IoT for worktrain/crane drivers and guides.
Improve safety on the network.
The watch warns the worktrain driver when he approaches a signal limiting his workzone.

## Slide 12: Tracking red mobile signals
IoT for worksite management and regulation enforcement.
GPS trackers are added to red mobile signals

## Slide 13: SAM Platform
SAM-IoT : Incoming data from devices
SAM-CEP : Event / time-series correlation
Measuring train input
SAM-P : Portal, webservices
SAM-DB : Storage and dataservices
SAM-AI: Deep- and
machine learning,
Video recognition

## Slide 14
AMDM
(Mobile)
Intranet webapps
Cloud apps
AMDx is an in-house developed software suite aiming to:
Manage linear asset measurement data
Automatically check business rules, create alerts and interact with work management system (RIAM…)
Offer a user friendly measurement analysis interface

## Slide 15: AMDM
Cloud app with useful tools for technicians
>1500 users, estimated 20 men days budget

## Slide 16: The linear location problem
Location of OCL problem

## Slide 17: The linear location problem

## Slide 18: The linear location problem
Antenne error: difference between pantograph and GPS antenna position
  Depends on specific installation, orientation of vehicle and direction of travel
  Error ~ 7m only in sense of travel
  How to improve: implement an IMU (to know vehicle orientation) and correct for distance (using a time based method)
GPS error: uncertainty of GPS position
  Depending on environment, weather (variable in time) and antenna position
  Error ~3m over all direction
  How to improve: implement an IMU to form a INS.
Sync error: synchronisation between GPS position and shock measurement
  Depending on travel speed
  Error ~ 4m (~100ms sync error) in approximate direction of travel
  How to improve: improve synchronisation algorithm

## Slide 19: The linear location problem
Then multiply this by the number of vehicle equipped with the measurement system..
Simplified location algorithms are OK for simple track layout where 27m uncertainty is fine (no switches, single track, …). But..
Advise:
  Determine alert groups based on possible error margins for a unique vehicle
  Then group the groups and take a smart average

## Slide 20: Questions?