## Slide 1: Digitalisation in maintenance (Big Data) @ Infrabel
Image recognition, AI & IOT projects
Pieter Verlinden
Lead Of Data Science@Infrabel.be

## Slide 2: Overview
Infrabel
Asset management information flow @ Infrabel
Smart projects overview

## Slide 3: Infrabel
We manage, maintain and modernise
the Belgian railway infrastructure
We coordinate rail traffic
on the Belgian network
~11k employees FTE
~800k passengers daily
~6500 km main track
~5800 km electrified
~4k switches
And we do it ourselves..

## Slide 4: SAM Platform
SAM-IoT : Incoming data from devices
SAM-CEP : Event / time-series correlation
Measuring train input
SAM-P : Portal, webservices
SAM-DB : Storage and dataservices
SAM-AI: Deep- and
machine learning,
Video recognition

## Slide 5
AMDM
(Mobile)
Intranet webapps
Cloud apps
AMDx is an in-house developed software suite aiming to:
Manage linear asset measurement data
Automatically check business rules, create alerts and interact with work management system (RIAM…)
Offer a user friendly measurement analysis interface

## Slide 6
Big data platform
Measurement
Data
Incident
Intervention
Malfunction
Asset Master data
Verified measurement results
Predictive notifications
Asset owner (expert) + data scientist
Technician
SAP EAM
Assets checked by
Measurement trains
Assets to be maintained
Model
Train Control
Computer
Interlocking
Computer
logs
SAMx
AMDx
Portal
Planner
Asset Management Information Flow

## Slide 7: OBMT
For 2018:
-> 3 commercial vehicles
-> 25000/30000 balises inspected
-> saves 25000 man hours / year
For 2019:
-> 20 commercial vehicles
IoT on commercial trains. Real time detection of ETCS equipment (LEU and eurobalise)
Real-time data to diagnostics system and processing by Operation Center
GPS
antenna
MVB bus
GSM antenna
Damaged balise
Connection
problem

## Slide 8: Switch
-> 400 switches equipped
-> Predictive maintenance
-> 75% of forecasts fail
-> Link with train routes traffic control
-> 50% of mechanical failures predicted
IoT on point machines. Real time monitoring of condition of turnout / railway switch
Real-time data to diagnostics system and processing by Operation Center
Worm gear
Bad alignment

## Slide 9: Switch
-> 400 switches equipped
-> Predictive maintenance
-> 75% of forecasts fail
-> Link with train routes traffic control
-> 50% of mechanical failures predicted
IoT on point machines. Real time monitoring of condition of turnout / railway switch
Real-time data to diagnostics system and processing by Operation Center
Wear on
Sliders

## Slide 10: Switch
-> AI
-> Deep learning / machine learning
-> Unsupervised-learning -> Dimensionality reduction using neural networks
IoT on point machines. Real time monitoring of condition of turnout / railway switch
Normal data
Over Current
Not locking

## Slide 11: Switch
-> 70 weather stations
-> Measuring weather
-> Environment characteristics
air and rail temperature
humidity and precipitation
(also the type , eg: snow)
predictions
Estimated savings
20 % on turnout energy bill
IoT on point machines. Real time monitoring of condition of turnout / railway switch
Off Medium High
20% less
heating
AI : Automatic change heating level by trained neural network

## Slide 12: Switch
-> target : 4000 switches
-> 1 automated control / year
-> data cel defect verification
-> laser measurements
-> HD video from different angles
-> saves 20000 man hours / year
Measuring train : Automated measuring and visual inspection of condition of turnout / railway switch
  5 cameras associated with 3 lasers per rail

## Slide 13: Pantograph shock detection
For 2018:
-> 11 commercial vehicles
-> More than 1M km inspected
-> 261k shock alerts received
-> Grouped to 22k locations
-> 472 workorders created
IoT on commercial trains. Real time detection of catenary problems.
Fully automated from alert to workorder

## Slide 14: CatVision
Home made vision systems for catenary applications

## Slide 15: Train monitoring system
Currently for one type pantograph:
3mm accurate carbon thickness
10% false/positive & false/negative
Deformation check

## Slide 16: SpadWatch
IoT for worktrain/crane drivers and guides.
Improve safety on the network.
The watch warns the worktrain driver when he approaches a signal limiting his workzone.

## Slide 17: AMDM
Cloud app with useful tools for technicians
>1500 users, estimated 20 men days budget

## Slide 18: Questions?